## Slide 1: Infineon & Raspberry pi in IoT
- restricted -
Swarnam Panday (IFIN DES TCP EPE)

## Slide 2: Agenda
IoT
Benefits & Architecture of IoT
Raspberry pi
Infineon & Raspberry pi in IoT
Components (Infineon)
Applications
Egg catcher game using Magnetic Sensor
Gesture recognition using Magnetic Sensor
1
2
3
4
5
6
1
2

## Slide 3: Agenda
Detecting wind speed using 2 barometric Pressure Sensor
Platform for exchanging knowledge
3
4

## Slide 4: Agenda
IoT
Benefits & Architecture of IoT
Raspberry pi
Infineon & Raspberry pi in IoT
Components (Infineon)
Applications
Egg catcher game using Magnetic Sensor
Gesture recognition using Magnetic Sensor
1
2
3
4
5
6
1
2

## Slide 5: IoT (Internet of Things)
Connecting everyday things embedded with electronics, software & sensors to the internet & among themselves enabling them to collect & exchange data.
A “thing” is any object with embedded electronics that can transfer data over a network – without any human interaction. Same thing if capable of taking decisions on its own without any human intervention then thing could be also referred to a “Smart Thing”.
Examples are-
Wearable devices
Environmental sensors
Machinery in factories
Devices in homes
Components in vehicles

## Slide 6: Agenda
IoT
Benefits & Architecture of IoT
Raspberry pi
Infineon & Raspberry pi in IoT
Components (Infineon)
Applications
Egg catcher game using Magnetic Sensor
Gesture recognition using Magnetic Sensor
1
2
3
4
5
6
1
2

## Slide 7: Benefits of IoT
Efficient resource utilization
Minimizes human effort
Saves time
Development of AI through IoT
Improved security
Benefits

## Slide 8: 5 Layer architecture
Manages the whole IoT system, including applications, business & profit
models & users privacy.
Stores, analyses & process huge amount of data. Create databases,
cloud computing & big data processing modules.
Responsible for delivering application specific service to the user.
Transfer the sensor data between different layer through networks such
as wireless, 3G, LAN, Bluetooth, RFID & NFC.
Business Layer
Application Layer
Processing Layer
Comm Layer
Sensors sense and gather information about the environment.
Perception Layer

## Slide 9: Agenda
IoT
Benefits & Architecture of IoT
Raspberry pi
Infineon & Raspberry pi in IoT
Components (Infineon)
Applications
Egg catcher game using Magnetic Sensor
Gesture recognition using Magnetic Sensor
1
2
3
4
5
6
1
2

## Slide 10: Raspberry Pi
The Raspberry Pi is a low cost, credit-card sized computer that plugs into a computer monitor or TV, and uses a standard keyboard and mouse.
Pi 1 Model A+
CPU: 700MHz 32-bit single-core ARMv6 RAM: 512MB** USB: 1 port Connectivity: None
Pi 2 Model B
CPU: 900MHz 32-bit quad-core ARMv8* RAM: 1GB USB: 4 ports Connectivity: Ethernet
Pi 3 Model B+
CPU: 1.2GHz 64-bit quad-core ARMv8 RAM: 1GB USB: 4 ports Connectivity: Ethernet, Wi-Fi, Bluetooth

## Slide 11: Raspberry Pi
Pi Zero
CPU: 1GHz 32-bit single-core ARMv6 RAM: 512MB USB: 1 micro USB OTG port Connectivity: Bluetooth and Wi-Fi
Pi 4 Model B
CPU: Quad core Cortex-A72 (ARM v8) 64-bit SoC @ 1.5GHz
RAM: 1GB, 2GB or 4GB LPDDR4-3200 SDRAM (depending on model)
USB: 2 USB 3.0 ports; 2 USB 2.0 ports.
2 × micro-HDMI ports (up to 4kp60 supported)
Connectivity: 2.4 GHz and 5.0 GHz IEEE 802.11ac wireless, Bluetooth 5.0, BLE, Gigabit Ethernet

## Slide 12: Possibilities with Raspberry Pi
It is a capable little device that enables people of all ages to explore computing, and to learn how to program in languages like Scratch and Python.
It’s capable of doing everything you’d expect a desktop computer to do, from browsing the internet and playing high-definition video, to making spreadsheets, word-processing, and playing games.
Raspberry Pi has the ability to interact with the outside world with help of sensors connected to its 40 GPIO pins & DSI display port CSI camera port.
Has been used in a wide array of digital maker projects, from music machines and parent detectors to weather stations.

## Slide 13: Agenda
IoT
Benefits & Architecture of IoT
Raspberry pi
Infineon & Raspberry pi in IoT
Components (Infineon)
Applications
Egg catcher game using Magnetic Sensor
Gesture recognition using Magnetic Sensor
1
2
3
4
5
6
1
2

## Slide 14: Infineon & Raspberry Pi in IoT
Cloud connectivity
Hardware
Software
Application
Cloud gateway
Multi cloud supported
TCP, HTTP, Restful API
MQTT
Interact with outer atmosphere
Infineon industrial Grade sensor
DPS, TLV, Microphone
Raspberry pi Adapter
Python Libraries for Infineon Sensors
Application layer
Example codes for different sensors
Edge processor
Media controller
Vision system
Data acquisition
Visualization
Controller
Infineon
Offering
Maker/ Industrial innovation

## Slide 15: Hardware and software blocks of ecosystem(current)
Rpi
Rpi adapter & Camera
Infineon Sensors
Bringing the “Internet of Things” with Raspberry pi to life requires a comprehensive system approach, inclusive of –
Intelligent processing and sensing technology
Connectivity
Software & services
Along with a leading ecosystem of partners

## Slide 16: Benefit of using Raspberry pi
Solution before python Libs
Solution after python libs

## Slide 17: Benefit of using Raspberry pi
Manages the whole IoT system, including applications, business & profit
models & users privacy.
Stores, analyses & process huge amount of data. Create databases,
cloud computing & big data processing modules.
Responsible for delivering application specific service to the user.
Transfer the sensor data between different layer through networks such
as wireless, 3G, LAN, Bluetooth, RFID & NFC.
Business Layer
Application Layer
Processing Layer
Transport Layer
Sensors sense and gather information about the environment.
Perception Layer
CLUBBED

## Slide 18: Agenda
IoT
Benefits & Architecture of IoT
Raspberry pi
Infineon & Raspberry pi in IoT
Components (Infineon)
Applications
Egg catcher game using Magnetic Sensor
Gesture recognition using Magnetic Sensor
1
2
3
4
5
6
1
2

## Slide 19: Shield2Go Adapter for Raspberry Pi
To be stacked on the top of raspberry pi, making pi compatible with S2Go format.
Compatible with Raspberry pi 3, 3B+, 4B and Zero.
Link

## Slide 20: Advantage of Adapter
Hassle of wires lead to multiple problems.
Avoid usage of wires and avoids loose connection.
Multiple sensors can be stacked at same time.

## Slide 21: Sensors compatible with Raspberry pi
DPS 310, 368, 422 -- Digital Pressure Sensor (GitHub Link)
TLV493D -- Magnetic Sensor (GitHub Link)
IM69D130 -- MEMS Microphone (GitHub Link)

## Slide 22: Agenda
IoT
Benefits & Architecture of IoT
Raspberry pi
Infineon & Raspberry pi in IoT
Components (Infineon)
Applications
Egg catcher game using Magnetic Sensor
Gesture recognition using Magnetic Sensor
1
2
3
4
5
6
1
2

## Slide 23: Agenda
IoT
Benefits & Architecture of IoT
Raspberry pi
Infineon & Raspberry pi in IoT
Components (Infineon)
Applications
Egg catcher game using Magnetic Sensor
Gesture recognition using Magnetic Sensor
1
2
3
4
5
6
1
2

## Slide 24: Egg catcher game

## Slide 25: Agenda
IoT
Benefits & Architecture of IoT
Raspberry pi
Infineon & Raspberry pi in IoT
Components (Infineon)
Applications
Egg catcher game using Magnetic Sensor
Gesture recognition using Magnetic Sensor
1
2
3
4
5
6
1
2

## Slide 26: Gesture recognition
3DSense Shield2Go
Raw data
to 2D
co-ordinates
Gaussian Filter

## Slide 27: Output

## Slide 28: Agenda
Detecting wind speed using 2 barometric Pressure Sensor
Platform for exchanging knowledge
3
4

## Slide 29: Wind speed measurement with two barometric Pressure sensors
Sensor A measures the barometric air pressure inside the device. The Sensor needs to be protected from the wind, but the device must not be completely air tight.
Sensor B measures the air pressure facing to the wind
The wind speed can be calculated with the air pressure values of sensor A and B
Sensor A
Sensor B
Wind
Device

## Slide 30: Agenda
Detecting wind speed using 2 barometric Pressure Sensor
Platform for exchanging knowledge
3
4

## Slide 31: Gitter
A platform for everyone to share their learnings & ideas related to that product.
While realizing any idea if one person faces the problem and he shares the it in chat other may help the person, that will save a lot of time and will enhance the maker culture IFIN & IFX wide.
Chat option will be available in the readme section of the repository in Infineon GitHub.

## Slide 32: Important links
GitHub link - https://github.com/Infineon
Python lib for DPS - https://github.com/Infineon/RaspberryPi_DPS
Chat room link for DPS - https://gitter.im/MakerConerFor_DPS/community?utm_source=badge&utm_medium=badge&utm_campaign=pr-badge
Python lib for TLV - https://github.com/Infineon/RaspberryPi_TLV
Chat room link for TLV - https://gitter.im/MakerConerFor_TLV493D/community?utm_source=badge&utm_medium=badge&utm_campaign=pr-badge
MEMS microphone – https://github.com/Infineon/GetStarted_IM69D130_With_RaspberryPi
Confluence link - http://confluencewikiprod.intra.infineon.com/pages/viewpage.action?pageId=190789474
Notes: Avoid abbreviation